## Slide 1
PROJECT
REVIEW – 2
Group Members:
Aathithya Pranav - CB.EN.U4ECE23002
Adarsh B - CB.EN.U4ECE23004
Ezhilkirthik M - CB.EN.U4ECE23016
Amrita Vishwa Vidyapeetham
Department of Electronics and Communication Engineering
23ECE381 Open Lab- 1
LDR Logic-Based Color Detection and Sorting System
Batch-A02​

## Slide 2
OBJECTIVE
1
  To design and implement color detection and sorting system.
  To accurately identify and classify up to seven colors (Red, Green, Blue, Cyan, Yellow, Magenta, White) using LDRs with RGB optical filters.
  To convert optical color signals into digital logic codes through comparators and decoders.
  To enable real-time automated sorting of objects on a conveyor system using servo motor mechanism
  To demonstrate a low-cost, reliable, and autonomous solution for industrial and laboratory applications.

## Slide 3
BLOCK DIAGRAM
02

## Slide 4
555 Timer IC
LM358 IC
BCD-to-7-segment decoder IC
03
8-channel analog multiplexer IC
Resistors
Potentiometers
Capacitors
Servo Motor
7 Segment Display (Cathode)
DSO
LDR
Components Used

## Slide 5
04
CIRCUIT DIAGRAM

## Slide 6
05
DESIGN
Comparator Design
-
+

## Slide 7
DESIGN
06
  Reference Circuit
Decoder Design
D C B A

## Slide 8
DESIGN FORMULAS
07
Astable Multivibrator:
  T_high​ = 0.693*C1​*(R1​+R2​)
  T_low​ = 0.693*C1*⋅R2​
  T = T_high ​+ T_low​
Monostable Multivibrator:
  T = 1.1*R*C
Resitor Ladder R Value:
  R = T/(1.1*C)

## Slide 9
DESIGN VALUES
08
Servo Rotation (°) | Pulse Width (ms) | Resistor Values (R) | T = 1.1*(R)*C
0 | 1 | 0 | 1
22.5 | 1.125 | 10.23K | 1.122
45 | 1.25 | 11.36K | 1.248
67.5 | 1.375 | 12.5K | 1.375
90 | 1.500 | 13.64K | 1.5
112.5 | 1.625 | 14.77K | 1.628
135 | 1.75 | 15.91K | 1.749
157.5 | 1.875 | 17.05K | 1.8755

## Slide 10
09
Analysis
7 Segment Display Code | Blue | Green | Red | Output | Servo Rotation (°) | Pulse Width (ms)
0 | 0 | 0 | 0 | Black | 0 | 1
1 | 0 | 0 | 1 | Red | 22.5 | 1.125
2 | 0 | 1 | 0 | Green | 45 | 1.25
3 | 0 | 1 | 1 | Yellow | 67.5 | 1.375
4 | 1 | 0 | 0 | Blue | 90 | 1.500
5 | 1 | 0 | 1 | Magenta | 112.5 | 1.625
6 | 1 | 1 | 0 | Cyan | 135 | 1.75
7 | 1 | 1 | 1 | White | 157.5 | 1.875

## Slide 11
10
Analysis

## Slide 12
11
REFERENCE
[1] I. Mazumdar, R. Mondal, and S. Pal, “Design and development of a low cost colour sensor and its application in angular position control system of a stepper motor,” Int. J. Electron. Comput. Sci. Eng., vol. 2, no. 4, pp. 1241–1251, 2013.
[2] T. K. Binnar, D. D. Deoghare, P. N. Patil, and V. S. Kulkarni, “Designing of RGB color detector,” Int. J. Recent Dev. Eng. Technol., vol. 3, no. 2, p. 12, Aug. 2014.
[3] M. Petersen et al., “Conveyor line color object sorting using a monochrome camera, colored light and RGB filters,” in Proc. 23rd Annu. Hawaii Int. Conf. Educ., Honolulu, HI, USA, Jan. 4–7, 2025.
[4] A. Amhani and Z. Iqbal, “Automated color sensor system using LDR and RGB LEDs controlled by Arduino,” ARPN J. Eng. Appl. Sci., vol. 12, no. 19, pp. 5532–5535, Oct. 2017.
[5] C. Tran, “Automobile tail lamp and brake lamp controller,” Analog Dialogue, vol. 43, Dec. 2009. [Online]. Available: C. Tran, "Automobile Tail Lamp and Brake Lamp Controller," Analog Dialogue, vol. 43, Dec. 2009. Available: https://www.analog.com/en/resources/analog-dialogue/articles/automobile-tail-brake-lamp-controller.html. [Accessed: Sep. 18, 2025].
[6] Virtual Labs, IIT Roorkee, “Astable and Monostable Multivibrator,” Virtual Labs. [Online]. Available: https://ae-iitr.vlabs.ac.in/exp/astable-monostable-multivibrator/theory.html. [Accessed: Sep. 18, 2025].